## Slide 1: Ch.3 - Computer Organization
BIT 1003 - Presentation 5

## Slide 2: Contents
REAL NUMBER FORMATS
INTEGER DATA FORMATS
COMPUTER WORD SIZE
DATA REPRESENTATION
VON NEUMANN ARCHITECTURE
CPU/ALU
CHARACTER FORMATS
MEMORY
INSTRUCTION SET

## Slide 3: VON NEUMANN ARCHITECTURE
Most computers today operate according to the “von Neumann architecture.”
The main idea of the von Neumann architecture is that the program to be executed resides in the computer’s memory, along with the program’s data.
John von Neumann published this idea in 1945.

## Slide 4: DATA REPRESENTATION
We’re used to representing numbers in “base 10.”
Why?

## Slide 5: DATA REPRESENTATION
1
42710= ?
2
3
42712= ?
42716= ?
42710= 4*100
2*10
+ 7*1
427
42712= 4*122
2*121
+ 7*120
60710
42716= 4*162
2*161
+ 7*160
106310

## Slide 6: BASE 2
Computers use base 2, because it’s easy to build hardware that computes based on only two states—on and off, one and zero.
Base 2 is also called the “binary number system,” and the columns in a base-2 number work the same way as in any other base.

## Slide 7
What is the base-10 value of the binary number 10011010?
128+16+8+2 = 15410
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
128 | 0 | 0 | 16 | 8 | 0 | 2 | 0

## Slide 8: “math facts” for binary math
Binary addition
0 + 0 = 0
0 + 1 = 1
1 + 1 = 10 (remember, this means 2; and also 0 carry 1 to the next column)

## Slide 9
Let’s add the binary value of 1100 to 0110:
1100 | (12 in base 10)
+ 0110 | (6 in base 10)
10010 | (18 in base 10)

## Slide 10: COMPUTER WORD SIZE
Guess next ^.^
64 Bit
32 Bit
16 Bit
8 Bit

## Slide 11: COMPUTER WORD SIZE
largest number
COMPUTER WORD SIZE (Bits) | largest number (binary) | largest number (base-10)
8 | 11111111 | 255
16 | 1111111 11111111 | 0 through 65,535 or −32,767 through 32,766
32 | … | 0 through 4,294,967,295 or −2,147,483,648 through 2,147,483,647
64 | … | ~trillion billions! (0 → +18446744073709551615)

## Slide 12: DATA FORMATS
Computers need to keep track of the sign (±) of a number.
and must also be able to represent fractional values (real numbers).
HOW?

## Slide 13: MSB - LSB
MSB: most significant bit
(en anlamlı bit)
LSB: least significant bit
for a 8 bit number:
MSB |  |  |  |  |  |  | LSB

## Slide 14: sign (±) of a number
unsigned
use msb to represent the most significat digit
of the number
signed / unsigned number
signed
use msb to represent the sign of the number
will be zero if the number is positive,
and 1 if the number is negative

## Slide 15: e.g.
Here is a positive 6 for an 8-bit computer:
00000110
How do we represent −6?
10000110 ?
That would be incorrect!

## Slide 16
What happens if we add 1 to that representation?
which would be −7, not −5!
10000110 | 
+ 1 | 
10000111 | =?

## Slide 17: “two’s complement”
Add one
Change all the zeros to ones and all the ones to
zeros
Take binary number
Phase 1
Phase 2
Phase 3
The correct representation of a negative number is called the “two’s complement” of the positive value.

## Slide 18: two’s complement of 6
00000110 | 11111001 | 11111001 | All the bits of +6 are “complemented” (reversed)
 |  | +00000001 | Add 1
 |  | 11111010 | The two’s complement of 6 = −6
Phase 1
Phase 2
Phase 3
Add one
Change all
0 1
1 0
Take binary number

## Slide 19: REAL NUMBER FORMATS
Real numbers consist of a mantissa and an exponent.
Computer designers decide how to allocate the bits of the computer word so that some can be
used for the mantissa and some for the exponent.
In addition, the mantissa can be positive or negative, and the exponent can be positive or negative.

## Slide 20: mantissa and exponent
Real numbers consist of a mantissa and an exponent.
  ± mantissa x 10 ± exponent
Computer designers decide how to allocate the bits of the computer word so that some can be used for the mantissa and some for the exponent.
The mantissa can be positive or negative, and the exponent can be positive or negative.

## Slide 21: Examples
123.45 can be represented as:
12345 × 10−2 | 
1.2345 × 10+2 | Scientific notation (normalized)
0.12345 × 10+3 | Language independent arithmetic standard

## Slide 22: The IEEE Standard for Floating-Point Arithmetic (IEEE 754)
The 32-bit format looks like this:
S | E | E | E | E | E | E | E | E | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m | m
Sign
Exponent
Mantissa

## Slide 23: exercise
How would we represent 8.510?
  1000.1
in scientific notation:
  1.0001 * 23
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3
 |  |  |  | 1 | 0 | 0 | 0 |  | 1 |  | 

## Slide 24
The IEEE 32-bit specification uses a “bias” of 127 on the exponent (this is a way of doing without a separate sign bit for the exponent)
exponent field will have the binary value of 127 + 3, or 130
After all this, the binary representation of 8.5 is:
01000001000010000000000000000000

## Slide 25: example
Calculate the number
sign is 0, so the number is positive;
expo is 124, so the true exponent is –3;
and fraction is .01.

## Slide 26: Double-precision 64 bit

## Slide 27: 32-bit single-precision examples:
Type | Sign | Exp | Exp+Bias | Exponent | Significand (Mantissa) | Value
Zero | 0 | -127 | 0 | 0000 0000 | 000 0000 0000 0000 0000 0000 | 0.0
Negative zero | 1 | -127 | 0 | 0000 0000 | 000 0000 0000 0000 0000 0000 | −0.0
One | 0 | 0 | 127 | 0111 1111 | 000 0000 0000 0000 0000 0000 | 1.0
Minus One | 1 | 0 | 127 | 0111 1111 | 000 0000 0000 0000 0000 0000 | −1.0
Smallest denormalized number | * | -127 | 0 | 0000 0000 | 000 0000 0000 0000 0000 0001 | ±2−23 × 2−126 = ±2−149 ≈ ±1.4 × 10−45
"Middle" denormalized number | * | -127 | 0 | 0000 0000 | 100 0000 0000 0000 0000 0000 | ±2−1 × 2−126 = ±2−127 ≈ ±5.88 × 10−39
Largest denormalized number | * | -127 | 0 | 0000 0000 | 111 1111 1111 1111 1111 1111 | ±(1−2−23) × 2−126 ≈ ±1.18 × 10−38
Smallest normalized number | * | -126 | 1 | 0000 0001 | 000 0000 0000 0000 0000 0000 | ±2−126 ≈ ±1.18 × 10−38
Largest normalized number | * | 127 | 254 | 1111 1110 | 111 1111 1111 1111 1111 1111 | ±(2−2−23) × 2127 ≈ ±3.4 × 1038
Positive infinity | 0 | 128 | 255 | 1111 1111 | 000 0000 0000 0000 0000 0000 | +∞
Negative infinity | 1 | 128 | 255 | 1111 1111 | 000 0000 0000 0000 0000 0000 | −∞
Not a number | * | 128 | 255 | 1111 1111 | non zero | NaN

## Slide 28: HW
REVIEW QUESTIONS:
3.1 – 3.7