## Slide 1: What is the Signal?
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING
A signal is defined as any physical quantity which carries some information and varies with respect to time, or any other independent variable.
Examples:
s1(t)=5t, s2(t)=20t2
s1(t) varies linearly with t (time)
s2(t) varies quadratically with t (time)
Spatial variables spatial coordinates in a plane.

## Slide 2
A signal with a single independent variable is called one-dimensional.
A signal with M independent variables is called M-dimensional.
Example: A black-and white-TV picture is a 3-dimensional signal. What are its independent variables?
Signals can be classified into 4 categories based on the characteristics of the independent variable(s) and the values they take.
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING

## Slide 3
Continuous-time and continuous-valued signals (analog signals)
(Both horizontal and vertical axes are continuous)
Example: Speech signals, radar signals, geophysical signals, biomedical signals of electrocardiogram (ECG)
p=f(t)
Discrete-time, continuous-valued signals
These types of signals are obtained by sampling analog signals.
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING

## Slide 4
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING
Sampling is the discretization of the horizontal axis.
Continuous-time, discrete-valued signals
These types of signals are obtained by quantization of analog signals.
Quantization is the discretization of the vertical axis.

## Slide 5
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING
Example: A black-and-white photograph
Discrete-time, discrete-valued signals (digital signals)
Digital signals are required for computers.

## Slide 6
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING

## Slide 7
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING
EXAMPLES OF CONTINUOUS SIGNALS (ANALOG SIGNALS)
İnfo: at time t=0 charged to V0 volts

## Slide 8
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING

## Slide 9
Copyright 2012 | Instructor: Dr. Gülden Köktürk | EED1004-INTRODUCTION TO SIGNAL PROCESSING
Information: approximate period of 11 years